| Department of the Environment | Facts About… |
| --- | --- |
|  | Approved Emissions Analyzers for Certified Emissions Repair Facilities |

The following Four and Five-Gas Analyzers have been approved for use in Certified Emissions Repair Facilities (five gas analyzers are indicated in bold font):

| Manufacturer | Model |
| --- | --- |
| Allen | 53-370, 53-500, 53-530, 53-700, 53-710 |
| Autologic | 310-0111, 310-0112, 310-0121, 310 Series |
| Bear | 40-200, 40-400, 40-401, 40-504, 42-090, 42-902, 42-903, 42-904(B) |
| CAS | 87-1100 |
| De Jaye | 6333, 6241 |
| Hamilton | 650EII, CEA-640, HTS-650, HTS-870, VEA 650(D), VTS 850EII |
| Infrared Industries | FGA4000XD |
| Interro | PDA5GB |
| Kent-Moore | J39982-MICRO |
| OTC | 3700 Series, 3800 Series, J39982, MICROGAS |
| Rotunda | 53-500, MCA-3000G |
| Snap-On | MT 3505, EEEA300A, EEEA305A, MODIS (with calibration software), MT3100(A), MT3105, MT3500(A) |
| Sun | DGA-1000, 1040, 1043, 1052, 1215, 1805-9, 1805Z, DGA1000, EEOS107 (08, 11, 30, 40), MCA3000, MCS2500, MCS4000, MEA-1500-04 |
| Vetronix | MTS 1100, PXA 1000, PXA 1100 |

Emissions Analyzer Calibration Gas Requirements

- All calibration gas bottles must be labeled with the analytical concentrations of each gas component contained within the bottle.  Each gas component must be named to within +2% accuracy, traceable to NIST Standard Reference Materials (SRMs).  This certification must be indicated on the calibration gas label.

- Calibration gas may not be used past the expiration date on the cylinder.

- Each bottle of calibration gas must be equipped with a functional pressure gauge, which reads in pounds per square inch (psi).  Please note when the pressure in the bottle drops below 25 psi, the analyzer may not calibrate accurately.

- Each bottle of calibration gas must be equipped with a functional regulator to achieve the proper flow rate for calibration, unless the analyzer is internally equipped with a flow regulator.

Page 2 of 2

Gas Analyzer Calibration Gas Recommendations

Use calibration gas recommended by the manufacturer of the analyzer.  If you experience problems with a standard blend, check with the manufacturer to see if a special blend is required.  Commonly recommended specifications are:

Component			        Specification			     5% Blend Tolerance

Propane			                 1200 ppm			     1140 - 1260 ppm

CO				                 4.0 %			               3.8 % - 4.2 %

CO2				        12.0 %			               11.40 – 12.60 %

and for the 5-gas analyzer:

NOx				        2000 ppm			     1900 – 2100 ppm

Local Gas Suppliers

The following companies may be able to provide calibration gas for gas analyzers at Certified Emissions Repair Facilities.  The State of Maryland cannot recommend one vendor over another vendor.  The vendors are listed for information only.  There is no requirement to purchase gas from any of these companies.

Emission Supply                                                           Roberts Oxygen Company, Inc.

705 A Old Westtown Road                                           17011 Railroad Street

West Chester PA  19382                                              Gaithersburg MD 20877

800-541-8370                                                            301-948-8100

http://www.emissionsupply.org                                   http://www.robertsoxygen.com

GTS – Welco, Inc. / Praxair                                          Air Liquide

8025 Dorsey Run Road                                               6141 Easton Road

Jessup MD  20794                                                      Plumsteadville PA  18949

410-796-8845 or                                                       877-715-8651 or

800-942-1148                                                           215-766-8860

http://www.gts-welco.com                                         http://www.alspecialtygases.com