## Slide 1: PA DEP/BRP, Radon Division
Mid-Atlantic States Radiation Conference
September 19, 2018
Targeted Survey
leads to HIGH HOMES
Denise Bleiler
Radiation Protection Program Supervisor
Patrick McDonnell, Secretary
Tom Wolf, Governor

## Slide 2
Objectives
Radon Basics
Targeted Surveys
High Development data
Continued Outreach
Geology
Challenges

## Slide 3
Rn-222 Characteristics, Implications
  Naturally Occurring- Occurs in all soil and rocks, worldwide.
  Colorless, odorless, tasteless- Out of sight, out of mind.
  Gas- Provides for transport and mobility.
  Half-life- ~ Four days
  Radioactive- Carcinogenic property, increases risk of Lung Cancer
DEP/BRP Radon Division

## Slide 4
More Basics
  Ambient Air: 0.4 pCi/L
  National Indoor Conc. (whole house avg.): 1.3 pCi/L
  U.S. EPA Guideline: 4 pCi/L
  PA Basement Avg.: 7.0 pCi/L
  PA First Floor Avg.: 3.5 pCi/L
DEP/BRP Radon Division
Notes: ER = (WL x 100)/ Rn

## Slide 5
Reference values
Radon Basics in Perspective
Radon Concentration | W.B. Effective Dose
0.4 pCi/L | 57 mRem/yr.
1.3 pCi/L | 173 mRem/yr.
4.0 pCi/L | 577 mRem/yr.
7.0 pCi/L | 1000 mRem/yr.
500 pCi/L | 72 Rem/yr.
Notes: Assumptions: ER equals 0.4, DCC equals 1000 mRem/WLM, time spent on first floor equals 6,132 hrs/yr, QF= 20, Tissue weighting factor equals 0.08.

## Slide 6
Targeted surveys- previous and ongoing
  Lehigh, Berks, York, Clearfield, Lancaster, Montgomery, Chester, Lackawanna, Potter, Luzerne, Dauphin, Cumberland, Lebanon, Bucks, ….
  These surveys are used to increase awareness in higher risk areas.
    Radon Data
    Geology
DEP/BRP Radon Division

## Slide 7
Letters sent | 512 | 
Tests supplied | 294 | 57%
Tests analyzed (to date) | 243 | 83%
* Figures current as of May 15, 2015
Our goal is for 100% response
Upper Saucon Twp Survey

## Slide 8
Upper Saucon Twp. Lehigh Co. Radon Survey
Radon Levels | Targeted Survey Data | State-Wide Data
< 4.0 pCi/L | 50.2% (128) | 60.8%
4.0 – 10.0 pCi/L | 23.9% (61) | 22.7%
10.1 – 20.0 pCi/L | 5.5% (14) | 9.2%
20.1 – 50.0 pCi/L | 6.3% (16) | 5.3%
50.1 – 100.0 pCi/L | 3.9% (10) | 1.3%
100.1 – 1,000.0 pCi/L | 6.7% (17) | 0.44%
> 1,000 pCi/L | 3.5% (9) | 
% > 4 pCi/L | 49.8% (127) | 39%
% < 4 pCi/L | 50.2% (128) | 60.8%
N = | 255 | 878,600
PA Radon Division

## Slide 10
Upper Saucon Twp. Survey Area

## Slide 12
Worked with Township
Initial Mailing (512)
Follow-up mailing (265) *
Reminder letters sent (three separate times) *
Final letter with enclosed test kit *
Local school district contacted
PA Dept. of Health updated *
Outreach Efforts
* Unique to this Survey

## Slide 13
Township Bldg. “Open House” *
State Rep. and State Sen. Informed *
Conference call with EPA Region III and Headquarters. *
DEP Press Release.
Two local builders informed.
Outreach Efforts- continued
* Unique to this Survey

## Slide 14
Outreach Efforts- continued
Town Meeting – Dec 4, 2014 *
  About 400 people in attendance
  At least 4 mitigators present
  Handed out over 100 radon test kits ( DEP and ALA)
Town Meeting – 2016 *
Continue to measure homes before occupancy *
* Unique to this Survey

## Slide 16
19 Results Greater than 1,000
17,518 pCi/L - highest in world
6,176 pCi/L
5,336 pCi/L
3,715 pCi/L
2,748 pCi/L-higher than index house

## Slide 17
DEP/BRP Radon Division
Pre-Mitigation (pCi/L) | Post-Mitigation (pCi/L) | Percent Reduction
3715 | 2.8 | 99.92
2748 | 2.0 | 99.92
2478 | 2.3 | 99.90
1951 | 2.4 | 99.87
1812 | 1.3 | 99.92
1545 | 1.9 | 99.87
1703 | 6.6 | 99.60
1611 | 5.8 | 99.60
1400 | 2.1 | 99.85
1295 | 1.6 | 99.87
1024 | 3.0 | 99.70
1244 | 1.1 | 99.91
1270 | 3.1 | 99.75
1267 | 3.6 | 99.71

## Slide 18
DEP/BRP Radon Division
Typical high development home, backyard, and basement excavation Gamma readings
Background Gamma (MicroR/hr)
Basement & first floor before mitigation- ~110
Outside yard- ~115 to 150
Basement excavation- ~100-360 & ~800-900
8-10 microR/hr = average PA outdoor

## Slide 19
Gamma Survey in basement excavation
Notes: Lot 7, Whispering Pines Development, basement excavation

## Slide 20
Soil/rock sample collection
Notes: Lot 7, Whispering Pines Development, Basement excavation

## Slide 21: Collecting a Soil Profile
Ongoing Soil and Rock
Sampling and Rad Analysis
Above data March 2015.
Typical soil and rock contain 1 pCi/g U and Ra on the average

## Slide 23
Epler Formation-Limestone, Dolomite
These extremely high radon levels are due to the unique geology of the area.
The Perfect Storm: Geology
Notes: Brecciated- rock formed from another rock that is broken and shattered.
Carbonate soils come from limestone's and Dolomite

## Slide 24
We put basements into the very elevated radium enriched soils
The Perfect Storm: Geology

## Slide 25
The Perfect Storm: Geology

## Slide 26
DEP/BRP Radon Division
Latest Tally in this development
82 homes and empty lots
19 Homes > 1,000 pCi/L
32 Homes between >100 pCi/L <1,000 pCi/L
12 Empty Lots

## Slide 27: Typical Home

## Slide 28
PA Radon Division

## Slide 29: Ambient Radon/Gamma
Location | Radon Conc. pCi/L | mrem/yr.
Lot 24-Street B | 2.1 | 651
Cul De Sac- Street B | 0.6 | 204
Street A | 2.2 | 462
Street A | 1.6 | 401
Street B | 3.1 | 389
Riegelsville (control) | 0.5 | 203
Township Bldg. (control) | <0.4 | 171
Harrisburg (control) | <0.4 | 154

## Slide 30
Challenges
Reaching EVERY homeowner
  One occupied home finally tested- ? mitigated
  One letter translated into Chinese and Mandarin- help from EPA
Builders installing mitigation systems
  Builder installing audible alarm on fan
  Homeowner maintaining system
Testing prior to occupancy
Minimal ambient testing - complete

## Slide 31
Conclusions
These high homes are showing 99% radon reduction
Elevated levels of radon can be fixed
Continued Outreach to increase awareness

## Slide 32
Questions?
DEP/BRP Radon Division
Contact Information: www.dep.pa.gov
Click Radiation Protection then click Radon
    800 237-2366
    717 783-3594